## Slide 1: Testing process and results of network bridging on STM32MP15

## Slide 2: Objective
Characterize performance capabilities of the MP15 platform in various bridge configurations
  Ethernet to USB Ethernet dongle (USB Host)
  Ethernet to USB RNDIS (USB OTG)
  USB Ethernet Dongle (USB Host) to USB RNDIS (USB OTG)
Capture network throughput as well as CPU load of the bridge platform

## Slide 3: Testing Methodology
STM32MP157A-EV1 platform as the bridging device
  Running OSTL 4.1 (starter image)
  Installed iperf3 with apt-get
    Version : iperf 3.11 (cJSON 1.7.13)
STM32MP157C-DK2 platform as the client device
  Running OSTL 4.1 (starter image)
  Installed iperf3 with apt-get
    Version : iperf 3.11 (cJSON 1.7.13)
Ubuntu (22.04.1) based PC as the server device
  Iperf version 3.9 (cJSON 1.7.13)
USB Ethernet dongle was TP-LINK USB3 to RJ45 adapter (model UE306)
  No additional drivers were installed

## Slide 4: Additional Information
Establish a bridge between multiple interfaces
  Gigabit Ethernet port
  External USB ethernet dongle (USB Host port)
  RNDIS USB networking device
Running iperf3 on two connected platforms
  PC is always the iperf3 server started with Iperf3 –s
  MP157C DK2 is always the iperf3 client started with iperf3 –c <PC IP Addr>
mpstat to capture CPU load during test
  mpstat 1 11 – sample the CPU load every second for 11 seconds
Referenced the links below for bridging information
  https://tldp.org/HOWTO/BRIDGE-STP-HOWTO/set-up-the-bridge.html
  http://engr.case.edu/liberatore_vincenzo/NetBots/usbnet.pdf

## Slide 5: Test Configurations
Test 1 – Sanity test : Confirm Bridge gigabit interface and network infrastructure
Test 2 – Sanity test : Confirm Client gigabit interface and network infrastructure
Test 3 – Performance limit test : USB ethernet dongle, PC Connection
Test 4 – Performance limit test : USB ethernet dongle, MP1 Connection
Test 5 – Performance limit test : RNDIS throughput from MP1 to PC (no bridging)
Test 6 – Bridge : Ethernet to USB (Host) Ethernet dongle
Test 7 – Bridge : Ethernet to USB (OTG) RNDIS
Test 8 – Bridge : MP1 USB (Host) Ethernet dongle to USB (OTG) RNDIS

## Slide 6: Test Results

## Slide 7: Test 1 – Sanity Test on Bridge Gb Interface
Purpose
  Confirm gigabit capability of MP1 Bridge
  Confirm gigabit capability of network hub
  Confirm gigabit capability of PC server
Bridge Configuration
  No Bridge configuration established
Results
  939 Mbits/sec
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
ETH
USB
ETH
USB
ETH
USB
USB
Hub

## Slide 8: Test 1 Results
root@stm32mp1:~# { mpstat 1 11 & }; iperf3 -c 10.0.0.197
Connecting to host 10.0.0.197, port 5201
[ 5] local 10.0.0.207 port 45520 connected to 10.0.0.197 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 112 MBytes 943 Mbits/sec 0 454 KBytes
[ 5] 1.00-2.00 sec 113 MBytes 941 Mbits/sec 0 454 KBytes
[ 5] 2.00-3.00 sec 111 MBytes 933 Mbits/sec 0 475 KBytes
[ 5] 3.00-4.00 sec 112 MBytes 941 Mbits/sec 0 475 KBytes
[ 5] 4.00-5.00 sec 112 MBytes 939 Mbits/sec 0 475 KBytes
[ 5] 5.00-6.01 sec 113 MBytes 941 Mbits/sec 0 475 KBytes
[ 5] 6.01-7.00 sec 111 MBytes 936 Mbits/sec 0 505 KBytes
[ 5] 7.00-8.00 sec 112 MBytes 943 Mbits/sec 0 505 KBytes
[ 5] 8.00-9.00 sec 111 MBytes 931 Mbits/sec 0 532 KBytes
[ 5] 9.00-10.00 sec 112 MBytes 941 Mbits/sec 0 532 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.00 sec 1.09 GBytes 939 Mbits/sec 0 sender
[ 5] 0.00-10.04 sec 1.09 GBytes 934 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/03/23 _armv7l_ (2 CPU)
16:54:46 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
16:54:47 all 1.23 2.47 33.33 0.62 0.00 8.64 0.00 0.00 0.00 53.70
16:54:48 all 0.56 0.00 24.16 0.00 0.00 12.92 0.00 0.00 0.00 62.36
16:54:49 all 1.16 4.07 30.81 0.00 0.00 7.56 0.00 0.00 0.00 56.40
16:54:50 all 0.62 0.00 24.38 0.00 0.00 5.62 0.00 0.00 0.00 69.38
16:54:51 all 1.76 1.76 31.18 0.00 0.00 13.53 0.00 0.00 0.00 51.76
16:54:52 all 0.57 0.00 23.30 0.57 0.00 13.64 0.00 0.00 0.00 61.93
16:54:53 all 0.56 1.69 29.38 0.00 0.00 14.12 0.00 0.00 0.00 54.24
16:54:54 all 0.00 0.00 26.45 0.00 0.00 3.23 0.00 0.00 0.00 70.32
16:54:55 all 0.57 1.71 30.86 0.00 0.00 13.71 0.00 0.00 0.00 53.14
16:54:56 all 1.92 0.00 26.28 0.00 0.00 1.92 0.00 0.00 0.00 69.87
16:54:57 all 0.00 2.04 3.06 0.00 0.00 1.53 0.00 0.00 0.00 93.37
Average: all 0.80 1.28 25.41 0.11 0.00 8.84 0.00 0.00 0.00 63.56

## Slide 9: Test 2 – Sanity Test on Gb Interface
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
Hub
ETH
USB
ETH
USB
ETH
USB
USB
Purpose
  Confirm gigabit capability of MP1 Client
Bridge Configuration
  No Bridge configuration established
Results
  938 Mbits/sec

## Slide 10: Test 2 Results
root@stm32mp1:~# { mpstat 1 11 & }; iperf3 -c 10.0.0.197
Connecting to host 10.0.0.197, port 5201
[ 5] local 10.0.0.181 port 57020 connected to 10.0.0.197 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 113 MBytes 948 Mbits/sec 0 393 KBytes
[ 5] 1.00-2.00 sec 113 MBytes 943 Mbits/sec 0 457 KBytes
[ 5] 2.00-3.00 sec 112 MBytes 940 Mbits/sec 0 457 KBytes
[ 5] 3.00-4.00 sec 111 MBytes 928 Mbits/sec 0 457 KBytes
[ 5] 4.00-5.00 sec 112 MBytes 939 Mbits/sec 0 457 KBytes
[ 5] 5.00-6.00 sec 112 MBytes 941 Mbits/sec 0 457 KBytes
[ 5] 6.00-7.00 sec 113 MBytes 943 Mbits/sec 0 457 KBytes
[ 5] 7.00-8.01 sec 111 MBytes 928 Mbits/sec 0 530 KBytes
[ 5] 8.01-9.01 sec 112 MBytes 941 Mbits/sec 0 530 KBytes
[ 5] 9.01-10.00 sec 110 MBytes 928 Mbits/sec 0 663 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.00 sec 1.09 GBytes 938 Mbits/sec 0 sender
[ 5] 0.00-10.05 sec 1.09 GBytes 932 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/03/23 _armv7l_ (2 CPU)
17:00:25 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
17:00:26 all 1.32 0.00 13.91 0.66 0.00 7.95 0.00 0.00 0.00 76.16
17:00:27 all 0.00 4.02 24.14 0.00 0.00 17.82 0.00 0.00 0.00 54.02
17:00:28 all 0.64 0.00 19.23 0.00 0.00 5.13 0.00 0.00 0.00 75.00
17:00:29 all 1.16 4.05 23.12 0.00 0.00 13.87 0.00 0.00 0.00 57.80
17:00:30 all 0.00 0.00 20.13 0.00 0.00 4.55 0.00 0.00 0.00 75.32
17:00:31 all 2.41 1.20 24.70 0.00 0.00 12.05 0.00 0.00 0.00 59.64
17:00:32 all 0.00 0.00 22.54 0.00 0.00 11.56 0.00 0.00 0.00 65.90
17:00:33 all 0.00 2.73 22.95 0.00 0.00 15.85 0.00 0.00 0.00 58.47
17:00:34 all 1.08 0.00 16.76 0.00 0.00 19.46 0.00 0.00 0.00 62.70
17:00:35 all 1.15 2.87 25.29 0.00 0.00 11.49 0.00 0.00 0.00 59.20
17:00:36 all 0.00 0.00 1.52 0.00 0.00 0.51 0.00 0.00 0.00 97.97
Average: all 0.69 1.38 19.30 0.05 0.00 11.03 0.00 0.00 0.00 67.55

## Slide 11: Test 3 – Performance Test PC USB Eth Dongle
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
Hub
ETH
USB
ETH
USB
ETH
USB
USB
Purpose
  USB Ethernet Dongle performance limit
    PC connection
Bridge Configuration
  No Bridge configuration established
Results
  838 Mbits/sec

## Slide 12: Test 3 Results
root@stm32mp1:~# { mpstat 1 11 & }; iperf3 -c 10.0.0.91
Connecting to host 10.0.0.91, port 5201
[ 5] local 10.0.0.207 port 47172 connected to 10.0.0.91 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 113 MBytes 945 Mbits/sec 0 458 KBytes
[ 5] 1.00-2.01 sec 100 MBytes 832 Mbits/sec 0 486 KBytes
[ 5] 2.01-3.00 sec 93.8 MBytes 793 Mbits/sec 0 486 KBytes
[ 5] 3.00-4.01 sec 92.5 MBytes 772 Mbits/sec 0 486 KBytes
[ 5] 4.01-5.00 sec 95.0 MBytes 799 Mbits/sec 0 486 KBytes
[ 5] 5.00-6.01 sec 93.8 MBytes 781 Mbits/sec 0 486 KBytes
[ 5] 6.01-7.00 sec 93.8 MBytes 794 Mbits/sec 0 486 KBytes
[ 5] 7.00-8.00 sec 94.5 MBytes 792 Mbits/sec 0 513 KBytes
[ 5] 8.00-9.00 sec 112 MBytes 941 Mbits/sec 0 543 KBytes
[ 5] 9.00-10.00 sec 111 MBytes 933 Mbits/sec 0 590 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.00 sec 1000 MBytes 838 Mbits/sec 0 sender
[ 5] 0.00-10.05 sec 998 MBytes 833 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/03/23 _armv7l_ (2 CPU)
17:11:14 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
17:11:15 all 3.12 0.00 35.16 0.00 0.00 9.38 0.00 0.00 0.00 52.34
17:11:16 all 0.00 1.20 30.72 0.00 0.00 24.70 0.00 0.00 0.00 43.37
17:11:17 all 0.00 0.00 22.61 0.00 0.00 28.64 0.00 0.00 0.00 48.74
17:11:18 all 0.00 2.51 29.65 0.00 0.00 25.13 0.00 0.00 0.00 42.71
17:11:19 all 0.00 0.51 22.22 0.00 0.00 28.28 0.00 0.00 0.00 48.99
17:11:20 all 0.00 2.01 30.65 0.00 0.00 24.12 0.00 0.00 0.00 43.22
17:11:21 all 0.00 0.00 23.74 0.00 0.00 27.27 0.00 0.00 0.00 48.99
17:11:22 all 0.00 2.01 32.66 0.00 0.00 23.62 0.00 0.00 0.00 41.71
17:11:23 all 1.33 0.00 33.33 0.00 0.00 20.67 0.00 0.00 0.00 44.67
17:11:24 all 1.24 1.86 34.78 0.00 0.00 25.47 0.00 0.00 0.00 36.65
17:11:25 all 0.00 0.00 3.57 0.00 0.00 2.55 0.00 0.00 0.00 93.88
Average: all 0.40 0.95 26.59 0.00 0.00 22.18 0.00 0.00 0.00 49.87

## Slide 13: Test 4 – Performance Test MP1 USB Eth Dongle
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
Hub
ETH
USB
ETH
USB
ETH
USB
USB
Purpose
  USB Ethernet Dongle performance limit
    MP1 connection
Bridge Configuration
  No Bridge configuration established
Results
  254 Mbits/sec

## Slide 14: Test 4 Results
root@stm32mp1:~# { mpstat 1 11 & }; iperf3 -c 10.0.0.197
Connecting to host 10.0.0.197, port 5201
[ 5] local 10.0.0.91 port 33862 connected to 10.0.0.197 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 30.0 MBytes 252 Mbits/sec 0 379 KBytes
[ 5] 1.00-2.00 sec 31.9 MBytes 268 Mbits/sec 0 438 KBytes
[ 5] 2.00-3.01 sec 30.2 MBytes 250 Mbits/sec 0 495 KBytes
[ 5] 3.01-4.00 sec 30.0 MBytes 254 Mbits/sec 0 495 KBytes
[ 5] 4.00-5.00 sec 30.4 MBytes 255 Mbits/sec 0 495 KBytes
[ 5] 5.00-6.00 sec 31.3 MBytes 262 Mbits/sec 0 495 KBytes
[ 5] 6.00-7.00 sec 31.4 MBytes 264 Mbits/sec 0 495 KBytes
[ 5] 7.00-8.00 sec 30.7 MBytes 258 Mbits/sec 0 495 KBytes
[ 5] 8.00-9.02 sec 30.5 MBytes 251 Mbits/sec 0 542 KBytes
[ 5] 9.02-10.04 sec 27.5 MBytes 226 Mbits/sec 0 542 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.04 sec 304 MBytes 254 Mbits/sec 0 sender
[ 5] 0.00-10.09 sec 304 MBytes 253 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/03/23 _armv7l_ (2 CPU)
17:13:45 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
17:13:46 all 1.00 2.50 17.00 0.00 0.00 44.50 0.00 0.00 0.00 35.00
17:13:47 all 0.00 0.00 8.15 0.00 0.00 51.09 0.00 0.00 0.00 40.76
17:13:48 all 0.00 1.03 13.85 0.00 0.00 50.26 0.00 0.00 0.00 34.87
17:13:49 all 0.00 3.06 18.88 0.00 0.00 35.20 0.00 0.00 0.00 42.86
17:13:50 all 0.00 2.05 13.85 0.00 0.00 48.72 0.00 0.00 0.00 35.38
17:13:51 all 0.00 0.00 7.94 2.12 0.00 48.68 0.00 0.00 0.00 41.27
17:13:52 all 1.01 2.02 12.12 0.00 0.00 50.00 0.00 0.00 0.00 34.85
17:13:53 all 0.53 0.00 6.32 0.00 0.00 50.00 0.00 0.00 0.00 43.16
17:13:54 all 0.51 1.01 13.64 0.00 0.00 50.00 0.00 0.00 0.00 34.85
17:13:55 all 0.00 0.00 33.33 0.00 0.00 17.17 0.00 0.00 0.00 49.49
17:13:56 all 0.00 1.02 7.65 0.00 0.00 1.02 0.00 0.00 0.00 90.31
Average: all 0.28 1.17 13.98 0.19 0.00 40.49 0.00 0.00 0.00 43.90

## Slide 15: Test 5 – Performance Test MP1 RNDIS Connection
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
Hub
ETH
USB
ETH
USB
ETH
USB
USB
Purpose
  Understand RNDIS performance limit
Bridge Configuration
  No Bridge configuration established
Results
  155 Mbits/sec

## Slide 16: Test 5 Results
root@stm32mp1:~# { mpstat 1 11 & }; iperf3 -c 192.168.7.49
Connecting to host 192.168.7.49, port 5201
[ 5] local 192.168.7.1 port 48490 connected to 192.168.7.49 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 18.9 MBytes 159 Mbits/sec 0 346 KBytes
[ 5] 1.00-2.00 sec 17.8 MBytes 149 Mbits/sec 0 458 KBytes
[ 5] 2.00-3.00 sec 19.3 MBytes 162 Mbits/sec 0 505 KBytes
[ 5] 3.00-4.00 sec 17.3 MBytes 145 Mbits/sec 0 600 KBytes
[ 5] 4.00-5.00 sec 19.0 MBytes 160 Mbits/sec 0 648 KBytes
[ 5] 5.00-6.00 sec 17.6 MBytes 148 Mbits/sec 0 742 KBytes
[ 5] 6.00-7.00 sec 19.7 MBytes 165 Mbits/sec 0 830 KBytes
[ 5] 7.00-8.00 sec 18.3 MBytes 154 Mbits/sec 0 830 KBytes
[ 5] 8.00-9.00 sec 19.2 MBytes 161 Mbits/sec 0 830 KBytes
[ 5] 9.00-10.00 sec 17.8 MBytes 149 Mbits/sec 0 872 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.00 sec 185 MBytes 155 Mbits/sec 0 sender
[ 5] 0.00-10.04 sec 183 MBytes 153 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/04/23 _armv7l_ (2 CPU)
15:18:41 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
15:18:42 all 1.02 0.00 7.61 0.00 0.00 47.21 0.00 0.00 0.00 44.16
15:18:43 all 0.00 1.02 8.67 0.00 0.00 50.51 0.00 0.00 0.00 39.80
15:18:44 all 0.51 0.51 3.59 1.03 0.00 49.74 0.00 0.00 0.00 44.62
15:18:45 all 0.00 1.49 10.40 0.00 0.00 49.01 0.00 0.00 0.00 39.11
15:18:46 all 0.00 1.02 2.04 0.00 0.00 51.02 0.00 0.00 0.00 45.92
15:18:47 all 0.00 1.49 8.96 0.00 0.00 49.75 0.00 0.00 0.00 39.80
15:18:48 all 0.00 0.00 1.55 0.00 0.00 51.55 0.00 0.00 0.00 46.91
15:18:49 all 0.00 1.02 7.11 0.00 0.00 50.76 0.00 0.00 0.00 41.12
15:18:50 all 0.00 0.52 0.00 0.00 0.00 52.08 0.00 0.00 0.00 47.40
15:18:51 all 0.00 1.03 6.19 0.00 0.00 51.03 0.00 0.00 0.00 41.75
15:18:52 all 0.00 0.00 1.02 0.00 0.00 5.08 0.00 0.00 0.00 93.91
Average: all 0.14 0.74 5.23 0.09 0.00 46.14 0.00 0.00 0.00 47.66

## Slide 17: Test 6 – Bridge Ethernet to USB Host
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
Hub
ETH
USB
ETH
USB
ETH
USB
USB
Purpose
  Bridge ethernet to USB Host
  USB Ethernet dongle connected to MP1 Bridge
Bridge Configuration
brctl addbr br0
brctl addif br0 eth0
brctl addif br0 eth1
ifconfig eth0 0.0.0.0
ifconfig eth1 0.0.0.0
ifconfig br0 up
Results
  189 Mbits/sec
  CPU was 54.65% IDLE

## Slide 18: Test 6 Results
root@stm32mp1:~# iperf3 -c 10.0.0.197
Connecting to host 10.0.0.197, port 5201
[ 5] local 10.0.0.207 port 48736 connected to 10.0.0.197 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 23.3 MBytes 195 Mbits/sec 21 410 KBytes
[ 5] 1.00-2.00 sec 22.2 MBytes 187 Mbits/sec 9 337 KBytes
[ 5] 2.00-3.00 sec 22.5 MBytes 189 Mbits/sec 0 385 KBytes
[ 5] 3.00-4.00 sec 22.6 MBytes 190 Mbits/sec 15 320 KBytes
[ 5] 4.00-5.00 sec 22.6 MBytes 189 Mbits/sec 0 369 KBytes
[ 5] 5.00-6.00 sec 22.5 MBytes 189 Mbits/sec 20 304 KBytes
[ 5] 6.00-7.00 sec 22.7 MBytes 191 Mbits/sec 0 355 KBytes
[ 5] 7.00-8.00 sec 22.5 MBytes 189 Mbits/sec 20 287 KBytes
[ 5] 8.00-9.00 sec 22.7 MBytes 191 Mbits/sec 0 342 KBytes
[ 5] 9.00-10.00 sec 22.1 MBytes 185 Mbits/sec 0 389 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.00 sec 226 MBytes 189 Mbits/sec 85 sender
[ 5] 0.00-10.04 sec 225 MBytes 188 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/03/23 _armv7l_ (2 CPU)
17:24:00 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
17:24:01 all 0.00 0.00 0.00 0.00 0.00 0.00 0.00 0.00 0.00 100.00
17:24:02 all 0.00 2.07 4.15 0.00 0.00 33.68 0.00 0.00 0.00 60.10
17:24:03 all 0.50 0.00 1.00 0.00 0.00 49.50 0.00 0.00 0.00 49.00
17:24:04 all 0.00 1.51 5.53 0.00 0.00 50.25 0.00 0.00 0.00 42.71
17:24:05 all 0.00 0.00 0.50 0.00 0.00 50.25 0.00 0.00 0.00 49.25
17:24:06 all 0.00 1.01 5.03 0.00 0.00 50.25 0.00 0.00 0.00 43.72
17:24:07 all 0.00 0.00 0.00 0.00 0.00 50.51 0.00 0.00 0.00 49.49
17:24:08 all 0.99 1.98 5.45 0.00 0.00 49.50 0.00 0.00 0.00 42.08
17:24:09 all 0.00 0.00 1.49 0.00 0.00 49.50 0.00 0.00 0.00 49.01
17:24:10 all 0.00 1.02 5.08 0.00 0.00 50.25 0.00 0.00 0.00 43.65
17:24:11 all 1.00 0.00 0.50 0.00 0.00 49.75 0.00 0.00 0.00 48.76
17:24:12 all 0.50 2.01 4.02 0.00 0.00 15.08 0.00 0.00 0.00 78.39
Average: all 0.25 0.80 2.72 0.00 0.00 41.58 0.00 0.00 0.00 54.65

## Slide 19: Test 7 – Bridge Ethernet to USB OTG
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
Hub
ETH
USB
ETH
USB
ETH
USB
USB
Purpose
  Bridge ethernet to USB OTG RNDIS
  USB cable connecting PC to MP1 Bridge
Bridge Configuration
brctl addbr br0
brctl addif br0 eth0
brctl addif br0 usb0
ifconfig eth0 0.0.0.0
ifconfig usb0 0.0.0.0
ifconfig br0 up
Results
  141 Mbits/sec
  CPU was 53.89% IDLE

## Slide 20: Test 7 Results
root@stm32mp1:~# iperf3 -c 10.0.0.38
Connecting to host 10.0.0.38, port 5201
[ 5] local 10.0.0.207 port 55622 connected to 10.0.0.38 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 18.5 MBytes 155 Mbits/sec 0 856 KBytes
[ 5] 1.00-2.00 sec 16.7 MBytes 140 Mbits/sec 0 1017 KBytes
[ 5] 2.00-3.00 sec 17.0 MBytes 142 Mbits/sec 0 1017 KBytes
[ 5] 3.00-4.00 sec 15.9 MBytes 133 Mbits/sec 0 1017 KBytes
[ 5] 4.00-5.00 sec 17.0 MBytes 142 Mbits/sec 0 1017 KBytes
[ 5] 5.00-6.00 sec 16.9 MBytes 142 Mbits/sec 0 1017 KBytes
[ 5] 6.00-7.00 sec 17.0 MBytes 142 Mbits/sec 0 1017 KBytes
[ 5] 7.00-8.00 sec 17.0 MBytes 142 Mbits/sec 0 1017 KBytes
[ 5] 8.00-9.00 sec 16.8 MBytes 142 Mbits/sec 0 1017 KBytes
[ 5] 9.00-10.00 sec 15.8 MBytes 133 Mbits/sec 0 1017 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.00 sec 169 MBytes 141 Mbits/sec 0 sender
[ 5] 0.00-10.09 sec 167 MBytes 139 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/03/23 _armv7l_ (2 CPU)
17:34:23 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
17:34:24 all 0.00 3.59 3.08 0.00 0.00 4.10 0.00 0.00 0.00 89.23
17:34:25 all 0.00 0.50 1.01 0.00 0.00 49.75 0.00 0.00 0.00 48.74
17:34:26 all 0.00 1.01 6.06 0.00 0.00 49.49 0.00 0.00 0.00 43.43
17:34:27 all 0.00 0.50 1.49 0.00 0.00 49.75 0.00 0.00 0.00 48.26
17:34:28 all 0.00 1.99 4.48 0.00 0.00 49.75 0.00 0.00 0.00 43.78
17:34:29 all 0.00 0.50 1.01 1.51 0.00 50.25 0.00 0.00 0.00 46.73
17:34:30 all 0.00 0.50 6.03 0.00 0.00 50.25 0.00 0.00 0.00 43.22
17:34:31 all 0.00 0.50 1.00 0.00 0.00 50.00 0.00 0.00 0.00 48.50
17:34:32 all 0.00 2.53 2.53 0.00 0.00 50.51 0.00 0.00 0.00 44.44
17:34:33 all 0.00 0.51 1.01 0.00 0.00 50.00 0.00 0.00 0.00 48.48
17:34:34 all 0.00 1.49 5.47 0.00 0.00 48.26 0.00 0.00 0.00 44.78
17:34:35 all 0.00 1.51 0.50 0.00 0.00 0.00 0.00 0.00 0.00 97.99
Average: all 0.00 1.26 2.81 0.13 0.00 41.92 0.00 0.00 0.00 53.89

## Slide 21: Test 8 – Bridge USB Host to USB OTG
MP1 Bridge
MP1 Client
USB ETH Dongle
PC Server
Hub
ETH
USB
ETH
USB
ETH
USB
USB
Purpose
  Bridge USB Host to USB OTG (RNDIS)
  USB Ethernet dongle connected to MP1 Bridge
  USB cable connecting PC to MP1 Bridge
Bridge Configuration
brctl addbr br0
brctl addif br0 eth1
brctl addif br0 usb0
ifconfig eth0 0.0.0.0
ifconfig usb0 0.0.0.0
ifconfig br0 up
MP1 Client Configuration
  Ipconfig eth1 10.0.0.54 up
PC Server Configuration
  Manual assignment of 10.0.0.78 address
Results
  143 Mbits/sec
  CPU was 54.37% IDLE

## Slide 22: Test 8 Results
root@stm32mp1:~# iperf3 -c 10.0.0.78
Connecting to host 10.0.0.78, port 5201
[ 5] local 10.0.0.54 port 54478 connected to 10.0.0.78 port 5201
[ ID] Interval Transfer Bitrate Retr Cwnd
[ 5] 0.00-1.00 sec 17.3 MBytes 145 Mbits/sec 0 277 KBytes
[ 5] 1.00-2.00 sec 16.9 MBytes 142 Mbits/sec 0 277 KBytes
[ 5] 2.00-3.00 sec 17.2 MBytes 144 Mbits/sec 0 277 KBytes
[ 5] 3.00-4.00 sec 16.8 MBytes 141 Mbits/sec 0 277 KBytes
[ 5] 4.00-5.00 sec 17.4 MBytes 146 Mbits/sec 0 277 KBytes
[ 5] 5.00-6.00 sec 16.7 MBytes 140 Mbits/sec 0 291 KBytes
[ 5] 6.00-7.00 sec 17.3 MBytes 145 Mbits/sec 0 291 KBytes
[ 5] 7.00-8.00 sec 16.9 MBytes 142 Mbits/sec 0 291 KBytes
[ 5] 8.00-9.00 sec 17.3 MBytes 145 Mbits/sec 0 291 KBytes
[ 5] 9.00-10.00 sec 16.8 MBytes 141 Mbits/sec 0 291 KBytes
- - - - - - - - - - - - - - - - - - - - - - - - -
[ ID] Interval Transfer Bitrate Retr
[ 5] 0.00-10.00 sec 171 MBytes 143 Mbits/sec 0 sender
[ 5] 0.00-10.05 sec 170 MBytes 142 Mbits/sec receiver
iperf Done.
Linux 5.15.67 (stm32mp1) 05/04/23 _armv7l_ (2 CPU)
13:10:43 CPU %usr %nice %sys %iowait %irq %soft %steal %guest %gnice %idle
13:10:44 all 0.00 2.01 4.52 0.00 0.00 0.00 0.00 0.00 0.00 93.47
13:10:45 all 0.00 0.00 1.00 2.99 0.00 49.75 0.00 0.00 0.00 46.27
13:10:46 all 0.00 2.01 5.03 0.00 0.00 50.25 0.00 0.00 0.00 42.71
13:10:47 all 0.00 0.00 0.50 0.00 0.00 50.00 0.00 0.00 0.00 49.50
13:10:48 all 0.50 2.01 3.52 0.00 0.00 50.25 0.00 0.00 0.00 43.72
13:10:49 all 0.51 0.00 0.00 0.00 0.00 50.00 0.00 0.00 0.00 49.49
13:10:50 all 0.00 1.01 6.03 0.00 0.00 50.25 0.00 0.00 0.00 42.71
13:10:51 all 0.00 0.00 0.51 0.00 0.00 49.49 0.00 0.00 0.00 50.00
13:10:52 all 0.00 2.50 4.50 0.00 0.00 50.00 0.00 0.00 0.00 43.00
13:10:53 all 0.00 0.00 0.00 0.00 0.00 49.75 0.00 0.00 0.00 50.25
13:10:54 all 0.00 2.02 4.55 0.00 0.00 50.51 0.00 0.00 0.00 42.93
13:10:55 all 0.00 0.00 0.50 0.00 0.00 1.01 0.00 0.00 0.00 98.49
Average: all 0.08 0.96 2.55 0.25 0.00 41.77 0.00 0.00 0.00 54.37

## Slide 23: Results Comparison
 | Test 1 | Test 2 | Test 3 | Test 4 | Test 5 | Test 6 | Test 7 | Test 8
Data TPut | 939 Mbits / Sec | 938 Mbits/sec | 838 Mbits/sec | 254 Mbits/sec | 155 Mbits/sec | 189 Mbits/sec | 141 Mbits/sec | 143 Mbits/sec
CPU IDLE % |  |  |  |  |  | 54.65 % | 53.89 % | 54.37 %
Test 1 – Sanity test : Confirm Bridge gigabit interface and network infrastructure
Test 2 – Sanity test : Confirm Client gigabit interface and network infrastructure
Test 3 – Performance test : USB ethernet dongle, PC Connection
Test 4 – Performance test : USB ethernet dongle, MP1 Connection
Test 5 – Performance test : RNDIS throughput from MP1 to PC (no bridging)
Test 6 – Bridge : Ethernet to USB (Host) Ethernet dongle
Test 7 – Bridge : Ethernet to USB (OTG) RNDIS
Test 8 – Bridge : MP1 USB (Host) Ethernet dongle to USB (OTG) RNDIS

## Slide 24
Find out more at www.st.com
You can personalize this
last page with a short link
(ex. www.st.com/shortlink)
You can find a complete list of st.com short links on this page:
http://seo.st.com/toolbox/shortcuts/